## Slide 1: IN723 BGP Lesson 7
Aggregation
Convergence

## Slide 2: Resources
Case Studies
http://www.cisco.com/c/en/us/support/docs/ip/border-gateway-protocol-bgp/26634-bgp-toc.html
Configuration Guide
http://www.cisco.com/c/en/us/td/docs/ios-xml/ios/iproute_bgp/configuration/15-mt/irg-15-mt-book.html
Command Reference
http://www.cisco.com/c/en/us/td/docs/ios-xml/ios/iproute_bgp/command/irg-cr-book.html
Aggregation
http://www.cisco.com/c/en/us/support/docs/ip/border-gateway-protocol-bgp/5441-aggregation.html

## Slide 3: Well-Known Discretionary: ATOMIC_AGGREGATE
The Atomic Aggregate attribute is used to indicate that routes have been summarized.
  Attribute warns that the received information may not necessarily be the most complete route information available.
Attribute is set to either True or False with “true” alerting other BGP routers that multiple destinations have been grouped into a single update.
  Router update includes its router ID and AS number along with the supernet route enabling administrators to determine which BGP router is responsible for a particular instance of aggregation.
  Tracing a supernet to its original "aggregator" may be necessary for troubleshooting purposes.

## Slide 4: Aggregate
Aggregation = advertise a single route that can represent many (summarisation)
An aggregate route cannot be created unless a more specific route of that address exists within the BGP table
Aggregates do not inherit attributes (by default)
By default the aggregate will be advertised along with the specifics

## Slide 5: Aggregate cont
e.g to advertise a summary and not the specifics
router bgp <AS>
aggregate address 100.0.0.0 255.0.0.0 summary-only
network 100.10.0.0 mask 255.255.255.0
Notes: A more specific route must exist in the BGP table. In this case it is sourced using the network statement.

## Slide 6: Aggregate cont …
To filter only a subset of the specifics use a suppress-map
router bgp <AS>
aggregate address 100.0.0.0 255.0.0.0 suppress-map BLOCK
network 100.10.0.0 mask 255.255.255.0
route-map BLOCK permit 10
match ip address 1
access-list 1 permit 100.20.0.0 0.0.255.255
access-list 1 permit 100.30.0.0 0.0.255.255

## Slide 7: Problems caused by aggregation
Loss of specific AS_PATH information from individual prefixes
Could cause routing loops
Router C is sending the aggregate (summary-only) 160.0.0.0 255.0.0.0 to Router D

## Slide 8: Aggregation cont …
RouterD# show ip bgp
BGP table version is 6, local router ID is 4.4.4.4
Status codes: s suppressed, d damped, h history, * valid, > best, i - internal
Origin codes: i - IGP, e - EGP, ? - incomplete
Network Next Hop Metric LocPrf Weight Path
*> 160.0.0.0/8 4.4.4.1 0 300 i
Note AS path shows only AS from point of aggregation
Other attributes have not been inherited

## Slide 9: Aggregation cont …
Use as-set command to configure aggregate to inherit AS_PATH from specific routes
aggregate-address <ip> <mask> summary-only as-set
RouterD# show ip bgp
BGP table version is 2, local router ID is 4.4.4.4
Status codes: s suppressed, d damped, h history, * valid, > best, i - internal
Origin codes: i - IGP, e - EGP, ? - incomplete
Network Next Hop Metric LocPrf Weight Path
*> 160.0.0.0/8 4.4.4.1 0 300 {200,100} i

## Slide 10: Aggregation cont …
Note the AS_PATH now includes the set {200,100} indicating the aggregate summarises routes that have passed through AS 100 & 200
The AS_SET is not used to determine a shortest path only loop prevention
The AS_SET command also causes the aggregate to inherit all attributes (MED, Communities etc) from the specifics

## Slide 11: Aggregation cont …
Atomic-aggregate attribute indicates that aggregation has occurred
Aggregator attribute indicates where it occurred – IP & AS
RouterC# show ip bgp 160.0.0.0
BGP routing table entry for 160.0.0.0/8, version 9
Paths: (1 available, best #1)
Not advertised to any peer
{200,100}, (aggregated by 300 4.4.4.1)
0.0.0.0 from 0.0.0.0 (4.4.4.1)
Origin IGP, localpref 100, weight 32768, valid, aggregated, local, atomic-aggregate, best, ref 2

## Slide 12: Aggregation cont …
To choose which routes to inherit attributes from
router bgp <AS>
aggregate-address <ip> <mask> as-set advertise-map <route-map>
To change attributes (using set command within the route-map)
router bgp <AS>
aggregate-address <ip> <mask> attribute-map <route-map>

## Slide 13: Aggregation cont …
Can be combined
Example – to advertise summary route only, inherit attributes from select routes and change the attributes
router bgp <AS>
aggregate-address <ip> <mask> as-set summary-only advertise-map <route-map> attribute-map <route-map>

## Slide 14: BGP Convergence
BGP does not utilise periodic updates. No expiring prefix related timers
Uses explicit withdrawal in triggered UPDATE messages to signal loss of path to neighbours
Implicit signalling = newer information for same prefix from the same peer replaces previously learned information
Notes: Main limiting factors for BGP convergence:
BGP table size
Transport level settings
Advertisement delay

## Slide 15: Convergence: scan-time
bgp scan-time <seconds>
The BGP scanner process walks the BGP table and validates BGP next hop values
Additionally responsible for conditional advertisement check and performing route dampening
The Max / Default value = 60 sec. Range = 5-60 sec
Lowering the scan-time, can greatly improve BGP convergence
Notes: Confirm with show ip bgp summary

## Slide 16: Convergence: Timers
timers bgp {keepalive} {holdtime}
Keepalive - Default is 60 seconds
Holdtime (dead) - Default is 180 seconds
Only holdtime value communicated in the BGP Open messages
Smallest configured holdtime value between BGP peers is chosen & used to determine the keepalive
Neighbor-level command overrides process-level
Notes: Peers negotiate to both use same holdtime (the lowest)
A minimum acceptable holdtime can be configured.

## Slide 17: Convergence: Timers
neighbour {ip} advertisement-interval {sec}
Minimum interval between sending of BGP routing updates
Lowering can improve convergence
Not suggested to use low value in flapping networks
The default (Considered high) = 5 sec for iBGP peers, 30 sec for eBGP peers
Notes: MRAI = minimum route advertisement interval
Recommendations as low as 5sec (ebgp) & 1 sec (ibgp)
OO/GWS = 8 24

## Slide 18: Fast External Fallover
bgp fast-external-fallover
Immediately reset eBGP peering sessions if link used to reach them goes down
Not always desirable to trigger a fallover every time interface state changes, ie flapping link
If BGP fast external fallover disabled, BGP will wait until hold time expires to reset peering session
Enabled by default
Notes: Not available for iBGP. iBGP relies on underlying IGP triggered withdrawls (next-hop address tracking)

## Slide 19: Fast Peer Deactivation
Monitors peering session of specified neighbour. Peering session will be deactivated as soon as the IP route to BGP peer’s IP address disappears from routing table
Improves BGP response time to adjacency changes, no longer relies on BGP scanning intervals
router bgp 45000
neighbor 192.168.1.2 remote-as 40000
neighbor 192.168.1.2 fall-over
Notes: Works with iBGP & eBGP